## Slide 1: Az adatok optimális helye HPC környezetben
Temesi Tibor
tibor@silicon.hu
Silicon Computers

## Slide 2: “The confluence of AI with traditional simulations is going to transform the very nature of high performance computing. That’s the thing that I think is going be yet another sea change in how we do science.”
Rick Stevens, Associate Lab Director, Argonne National Laboratory
www.nextplatform.com/2019/10/22/exascale-is-not-your- grandfathers-hpc
“We’re not doing our grandfather’s HPC here.”

## Slide 3: SIMULATION + AI = OVER- PROPORTIONAL STORAGE GROWTH
HPC Storage spending is forecasted to grow with a 40% higher CAGR than HPC Servers through 2024.
Projected Compound Annual Growth Rate for customer spending 2019–2024
% CAGR
10%
9%
8%
7%
6%
5%
12.1%
4%
3%
2%
1%
0%
HPC Storage HPC Server
Source: Hyperion Research, 2019 Market Results, New Forecasts and HPC Trends, April 2020
14%
13%
12%
11%
 |  | 8.7% |  | 

## Slide 4: INPUT/OUTPUT PROFILES COULD NOT BE MORE DIFFERENT Era of convergence of traditional simulation and AI requires NEW HPC storage
Traditional simulation
Machine Learning
INPUT DATA
ALGORITHM
OUTPUT
INPUT DATA
HISTORICAL OUTPUT
ALGORITHM
+
+
CPU nodes
GPU nodes
Mainly WRITING PETAbytes of LARGE FILES in SEQUENTIAL order @ extreme speed
Mainly READING TERAbytes of FILES OF ALL SIZES in RANDOM order @ extreme speed

## Slide 5: START ANYWHERE, GO TO WHEREVER YOU
NEED
5
Nearly 10 TB/sec and > 700 PB capacity*
simulations for quantum computers, nuclear energy systems, fusion reactors, and precision medicines. 2021-2022
> 4 TB/sec and 30PB (All Flash) capacity*
NESAP enhance simulation, data processing, and machine learning applications
All Flash base rack: > 1TB/sec and up to 4.5 PB capacity*
Expansion rack: > 2 TB/sec and 4.6 PB*
Disk base rack: 90 GB/sec and 7.5 PB capacity*
Expansion rack: 120 GB/sec and 10 PB*
*usable capacity
2.5 TB/sec and ~ 400 PB capacity*
nuclear stockpile, secondary national security missions, nuclear nonproliferation and counterterrorism
2023
2.5 TB/sec and ~ 100 PB capacity*
LUMI - Large Unified Modern Infrastructure
2021
1 TB/sec and ~ 200 PB capacity*
All Flash entry point (6U)
Up to 80/50 GB/sec read/write
and 115 TB capacity*
Disk entry point
(10U):
15 GB/sec and
315 TB capacity*
cancer research, materials science, climate science, and cosmology
2H 2021
1 TB/sec and ~ 1 PB (All Flash) capacity*
IT4I – Astrophysics, Eng., Chemistry, Material Earth Live science
1H 2021
240 GB/sec and ~ 14.5 PB capacity*
2H 2020

## Slide 6: EXASCALE KÖVETELMÉNYEK
Erősebb „motorok”
Jobb kommunikáció: protokoll, hálózat, …
Alkalmazás-orientált architektúrák

## Slide 7: EXASCALE KÖVETELMÉNYEK …
Az adatok feldolgozása
  A cél, hogy az adat minél közelebb legyen a processzorhoz, amikor éppen dolgozik vele.
  Az adatok olvasási/írási sebessége: nem optimális, ha motorok „gyorsan várnak” az adatra.
  Nyilván nem lehet minden adat a processzor chipek belső cache memóriájában, akkor hol legyen?
  „Ki” mozgassa az adatokat?

## Slide 8: MEMÓRIÁK
Processzor belső cache
Külső memóriák:
  DRAM (32 bit bus),
  HBM (4096 bit bus): sok adat (AI) -> szélesebb adatutak (HBM memóriák), kisebb késleltetések

## Slide 9: TÁROLÓK
Közös, megosztott, többrétegű tárolórendszer
  Az éppen feldolgozandó adatok számára maximális írás/olvasási teljesítmény: SCRATCH: all-
flash, NVMe, ..
  Tárolási kapacitás az operatív adatok számára: HOME: HDD
  Archív réteg: szalagkönyvtár
  Automatizált adatmenedzsment

## Slide 10: NON-VOLATILE MEMORY EXPRESS (NVMe)
is fast, scalable, and efficient
Designed to move beyond HDDs
Standard interface for Solid State Media
A new protocol
Media?
Built for high performing storage devices | Leverages PCIe for lower latency, higher IOPS than SATA or SAS | New streamlined protocol and command-set (replaces SCSI) | No, its not high performance media— it’s a protocol to access to it!
A new storage protocol focused on
SSDs, replaces traditional I/O stacks
built on SCSI protocol, which is optimized for spinning media.
It leverages PCIe instead of SAS/SATA for greater bandwidth, IOPS and reduced latency

## Slide 11: TÁROLÓK
Közös, megosztott, többrétegű tárolórendszer
  Az éppen feldolgozandó adatok számára maximális írás/olvasási teljesítmény: SCRATCH: all-
flash, NVMe, ..
  Tárolási kapacitás az operatív adatok számára: HOME: HDD
  Archív réteg: szalagkönyvtár
  Automatizált adatmenedzsment

## Slide 12: THREE BASIC FILE SYSTEM CONFIGURATION OPTIONS
All HDD file system
/lustre
SSU-D2 (10U)
Up to 30 GB/sec from 212 HDD
SSU-D4 (18U)
Up to 40 GB/sec
from 424 HDD
. . .
Specifications per rack:
Up to 120 GB/sec (read/write)
Up to 10 PB usable capacity (16 TB HDD)
Scalable Storage Units (SSU)
All Flash file system
/lustre
. . . Specifications per rack: Up to 1,600 GB/sec (read) Up to 1,000 GB/sec (write) Scalable Storage Unit (SSU) SSU-F (2U) Up to 80 GB/sec sequential read from 24 SSD Up to 50 GB/sec sequential write from 24 SSD
Hybrid file system | 
/lustre | 
/lustre/disk | /lustre/flash
. . . . . . Disk and Flash pools in the same namespace with Cray ClusterStor data services providing capacity from Disk and performance from Flash | 

## Slide 13: BASIC LUSTRE
Object Storage Object Storage Target (OST) Target (OST)
Object Storage Servers (OSS)
Add’l MetaData Units
Metadata Metadata Target (MDT) Target (MDT)
MetaData Unit
++XX,000 Metadata Ops
++XX,000 Metadata Ops
MetaData Servers (MDS)
Storage Servers grouped
into failover pairs
Disk Object Storage
Unit
++ XX GB/s and PB
++ XX GB/s and PB
Management Network
DATA NETWORK (LNET)
Infiniband, Ethernet
Target 1
Target 2
System Management
MetaData Server (MDS)
Management Server (MGS)
System Manager Server 2
System Manager Server 1
LNET Router
Lustre Clients
Gateway
Metadata Target (MDT)
Metadata Target (MDT)
CIFS/NFS Clients
Object Storage Object Storage Target (OST) Target (OST)
Flash Object Storage
Unit
++ XX GB/s and TB
++ XX GB/s and TB
Object Storage Servers (OSS)
Typical Lustre components

## Slide 14: CLUSTERSTOR E1000 LUSTRE FILE SYSTEM & DMF V7
Object Storage Object Storage Target (OST) Target (OST)
Object Storage Servers (OSS)
Add’l MetaData Units
(AMDU)
Metadata Target (MDT)
Metadata Target (MDT)
MetaData Unit (MDU)
++XX,000 Metadata Ops
++XX,000 Metadata Ops
MetaData Servers (MDS)
Storage Servers grouped
into failover pairs
Disk Scalable Storage
Units (SSU-D)
++ XX GB/s and PB
++ XX GB/s and PB
Management Network
DATA NETWORK (LNET)
Infiniband, Ethernet, Slingshot
System Management Unit (SMU)
Target 1 Target 2
MetaData Server (MDS)
Management Server (MGS)
System Manager Server 2
System Manager Server 1
LNET Router
Lustre Clients
Gateway
Metadata
Target (MDT)
Metadata Target (MDT)
CIFS/NFS Clients
Data Management Framework v7
ClusterStor Data Service (CDS)
Object Storage Object Storage Target (OST) Target (OST)
Flash Scalable Storage
Unit (SSU-F)
++ XX GB/s and TB
++ XX GB/s and TB
Object Storage Servers (OSS)
Search/Policy Engine, Data Movers
ClusterStor Manager, VIEW
E1000 Solution

## Slide 15: SZALAGKÖNYVTÁR
Az adatok megőrzése, archiválása, biztonsági másolata

## Slide 16: TFINITY EXASCALE - ENTERPRISE ARCHIVE
TFinity Delivers
Over 1 Exabyte native capacity with LTO-9
Up to 858 PB native capacity with TS1160
24 x 7 x 365 operations
Dual robotics for availability and performance
Flexible Configurations
  3 to 45 frames
  100 to over 56,400 LTO slots/42,930 TS slots
  2 to 144 tape drives
LTO-9, LTO-8, LTO-7, TS1160, TS1155, TS1150, T10K
Technology
Upgrade in 10 LTO or 9 TS slot increments
400 mounts per hour

## Slide 17: TERAPACK ARCHITECTURE
Industry leading density
Industry’s smallest footprint
  Reduce floor space requirements
  Reduce tape handling
  10 LTO or 9 TS11xx tapes per TeraPack
TeraPack design allows TFinity to maximize the floor
space needed for the tape archive.
TeraPacks make moving media much more efficient
  Both in the TFinity and when transporting or moving tapes outside the library

## Slide 18: STANDARD BLUESCALE SOFTWARE FEATURES
Media Lifecycle Management (MLM) – Media Health reporting
Drive Lifecycle Management (DLM) – Drive Health reporting and diagnostics
Hardware Health Management (HHM) – Library Hardware reporting and diagnostics
Standard Encryption – Built in Encryption Key Management
Data Integrity Verification (DIV) – Verify data on tape automatically as a background task without host system involvement
AutoSupport – The library will automatically create a support ticket if any critical event is
encountered
Partitioning – Support for up to 16 partitions
Remote Library Connection (RLC) – Manage the library from anywhere through the same interface that is presented on the front panel touchscreen
Auto Drive Clean – Let the library automatically clean tape drives when they request to be cleaned

## Slide 19: Compatible with all major ISV software

## Slide 20: Spectra Logic HPC Customer References Europe

## Slide 21: HPC/AI COMPUTE & STORAGE HPC Storage Supports an Optimized Compute Experience for Active Workloads
HPC/AI Compute Cluster
High-Performance Storage
Scale-out NAS
Parallel File Systems
All-Flash File System

## Slide 22: INTRODUCING DATA MANAGEMENT FRAMEWORK VERSION 7 DMF Enables Data Curation, Placement and Protection Over Time & Distance
Active Tier Hot Data Front End
Perpetual Tier Warm/Cool Data
Backend
HPE Data Management Framework
Tiered data management
Tape
DMF
zero watt storage
Object Storage & Cloud
HPC/AI Compute Cluster
High-Performance Storage
Scale-out NAS
Parallel File Systems
All-Flash File System

## Slide 23: DMF INTEGRATION WITH TAPE STORAGE
Still the world’s most cost effective Storage @ 1¢ per GB
DMF is certified with libraries from HPE, as well as Spectra Logic, IBM and Oracle (StorageTek)
  Streams to tape drive at native rates, even for small files
  Block ID positioning for fast seek
Support for latest LTO-9 and Enterprise-class drive technology
Advanced feature support for accelerated retrieval and automated library management
  Supports Data Integrity Verification (DIV) and Logical Block Protection (LBP) available with Oracle T10k as well as IBM LTO and TS drives
  Recommended Access Order (RAO) and
SpectraLogic’s TAOS
LTO-8 12TB 360MB/s
TS1160 20TB 400MB/s

## Slide 24: DATA MANAGEMENT FRAMEWORK VERSION 7 Resolve Data Challenges with Data Management
Hierarchical storage management:
Integrated policy engine allows tiered data model with automated data movement to appropriate data tier, e.g. SSD/Flash tier for active data, tape and cloud for dormant/archive data
Maximize resources with automatic archival of stale or cold data
Data Protection Strategy
Safeguard petabytes of data with integrated, continuous backups
Maintain data integrity via self-describing media format and data checksums
Optimize Storage Utilization
Control Storage Costs:
– Minimize TCO by moving data to most cost-effective tier for desired access level,
i.e. from flash to HDD to tape to cloud
Scale storage acquisitions incrementally depending on need, i.e. more flash for active data, more tape for archive depending on demand
Protect and future-proof data with automated migration to new storage infrastructure
Manage Costs
Accelerate workflows:
Simplify management of large file collections with data set labeling
Construct data sets using file metadata including extended attributes
Automate data workflows with integrated job scheduling
Streamline data recovery with automatic
file versioning and Point-in-Time restore
Reduce manual intervention:
Reduce script writing and script maintenance
Reduce operator errors with automatic data movement
Streamline Workflows

## Slide 25: Köszönöm